Important Safety Instructions

1) Read these instructions.

2) Keep these instructions.

3) Heed all warnings.

4) Follow all instructions.

5) Do not use this apparatus near water.

6) Clean only with dry cloth.

7) Do not block any ventilation openings, install in accordance with the instructions.

8) Do not install near any heat sources such as radiations, heat registers, stoves, or other apparatus (including amplifiers) that produce heat.

9) Do not defeat the safety purpose of the polarized plug. If the provided plug does not fit into your outlet, consult an electrician for replacement of the obsolete outlet.

10) Protected the power cord from being walked on or pinched particularly at plugs, convenience receptacles, and the point where they exit from the apparatus.

11) Only use attachments/accessories specified by the manufacturer.

12) Unplug this apparatus during lighting storms or when unused for long periods of time.

13) Refer all servicing to qualified service personnel. Servicing is required when the apparatus has been damaged in any way, such as power-supply cord or plug is damaged, liquid has been spilled or objects have fallen into the apparatus, the apparatus has been exposed to rain or moisture, does not operate normally, or has been dropped.

|  | This marking indicates that this product should not be disposed with other household wastes throughout the EU. To prevent possible harm to the environment or human health from uncontrolled waste disposal, recycle it responsibly to promote the sustainable reuse of material resources. To return your used device, please use the return and collection systems or contact the retailer where the product was purchased. They can take this product for environmental safe recycling. |
| --- | --- |

14) Mains plug is used as the disconnect device, the disconnect device shall remain readily operable.

15) The ventilation should not be impeded by covering the ventilation openings with items, such as newspapers, table-cloth, curtains, etc.

16) No naked flame sources, such as lighted candles, should be placed on the apparatus.

17) Attention should be drawn to the environmental aspects of battery disposal.

18) The use of apparatus in moderate climate.

19) The apparatus shall not be exposed to dripping or splashing and that no objects filled with liquids, such as vases, shall be placed on the apparatus.

WARNING: To reduce the risk of fire or electric shock, do not expose this apparatus to rain or moisture.

WARNING: The batteries shall not be exposed to excessive heat such as sunshine, fire or the like.

WARNING: You must peel off the membrane of the top cover before using.Or it would harm your receive box without emitting its heat.

The symbol indicates that dangerous voltages constituting a risk of electric
shock are present within this unit.

The symbol indicates that there are important operating and maintenance
instructions in the literature accompanying this unit.

This symbol indicates that this product incorporates double insulation
between hazardous mains voltage and user accessible parts. When
servicing use only identical replacement parts.

CAUTION: When the apparatus was in electrostatic circumstance, it may be malfunction and need to reset by user.

WARNING: The USB memory stick should be plugged in the unit directly.
USB extension cable should not be used to avoid failing of data transferring
and interference caused.

Table of contents

1 Panel	1

1.1 Front Panel	1

1.2 Rear Panel	1

2 Remote Control	1

2.1 Key introduce	1

2.2 Installing the Battery	2

3 Connections	2

4 First Installation	3

4.1 Channel	3

4.2 AV	3

4.3 Installtion	3

4.4 Preference	3

4.5 Setting	3

4.6 Media:	3

5. Troubleshooting	4

6. Technical Specifications	5

# 1 Front and Rear Panel

## 1.1 Front Panel

## 1.2 Rear Panel

- ANT IN: This socket connects to your external Aerial.

- LOOP OUT: Used to connect another unit’s ‘ANT IN’ port.

- HD OUT: High definition audio and video output used to connect to a HD device.

- CVBS:This socket outputs composite video signal.

5)   AUDIO L/R: This socket outputs analog audio L/R signal.

6)   DC IN: This is used to connect to your adaptor.

# 2 Remote Control

## 2.1 Key introduce

- STANDBY: Switch the unit to on or standby.

- COLOUR BUTTONS:

(RED: no function;    (Green: witch resolution;

(Yellow: Switch aspect ratio;   (Blue: Timer setting;

- FWD: Searches forwards during media play.

- REV: Searches backwards during media play.

- PAUSE: Pauses media play.

- PLAY: Starts or resumes media play.

- TEXT: Displays Teletext Information.

- SUBTITLE: Selects Subtitles Language.

- EPG: (Electronic Program Guide)Turns the program guide on.

- UP / DOWN: Navigates through the Menus. Selects the next or previous Channel.

- RIGHT/LEFT: Navigates through the Menus. Increases or decreases volume.

- MENU: Turns on Main Menu.

- FAV: Turns on Favourite Menu.

- VOL+/-: Increases or decreases volume.

- 0-9 (Numeric Buttons): Selects a channel or setting.

- V-FORMAT: Video display scale.

- MUTE: Mute or Restore Audio Output.

- PREV: Skips to the previous track during playing media.

- NEXT: Skips to the next track during playing media.

- STOP: Stops media play.

- USB: Used to display a list of programs recorded on the current disc.

- RECALL: Used to switch between the last two viewed channels.

- AUDIO: Selects an Audio Language or Audio Mode.

- INFO: Displays additional channel information.

- OK:Confirms an entry or selection. Displays the list of channels.

- EXIT: Exits the current Menu or returns to the previous Menu.

- PAGE+/ -: Page up,Page down.

- REC: Used to record the program.

- TV/RADIO: Switches from TV function to Radio function and from Radio to TV.

## 2.2 Installing the Battery

Remove the battery cover from the Remote Control and put 2xAAA size batteries inside the compartment.

The diagram inside the Battery Compartment shows the correct way to install the batteries.

# 3 Connections

Caution: Make sure to check the voltage specification of the wall outlet is the same rating with the receiver. To prevent the risk of electric shock, do not open the cover or the back of the receiver.

Note: When connecting the receiver to other equipment, e.g., TV, VCR and amplifier, make sure to refer to relevant user manual for instruction. Also, make sure you disconnect all the equipments from the mains supply before the connection.

# 4 First Installation

After all connections have been made properly, switch on TV and make sure the receiver is connected to the Main Power. Press Power button to switch receiver on. If you are using the receiver for the first time or restored to Factory Default, the Main Menu will appear on your TV screen.

(1) Select [OSD Language] and press RIGHT/LEFT key to select an language.

(2) Select [Country] and press RIGHT/LEFT key to change frequency list .

(3) Select [Frequency Channel] and press RIGHT/LEFT key to test signle.

(4) Select [Channel Search] and press OK to start Search Channel.

## 4.1 Channel List

To access the Menu, press the MENU button and select [Channel List]. The Menu provides options to adjust the Channel Manage Settings. Select an option and press OK or RIGHT to adjust that setting. Press the EXIT button to exit the Menu.

4.1.1 TV Channel List/Radio Channel

To manage your program preferences (lock, edit, move or delete), you will need to enter the Channel Manager Menu.

Lock Channel
You can lock selected programs for restricted view. Lock a TV Program:

1.Press RED button the select the preferred program,and you should input ‘0000’to disappear the password box and then a lock- shaped symbol will display. The program is now marked as locked.
2. Repeat the previous step to select more programs.
3. To confirm and exit the menu, press the EXIT button.
4. Press the RED button to disable the locked program.
5. To view the locked program, you will be required to enter either the default password '0000' or your last set password.

Skip Channel

- Press GREEN button, then select the program you would like to skip, skip symbol will display.

- Press GREEN button, the program is marked as a skip.

Move Channel
1. Press YELLOW button, then select the program you would like to move, move symbol will display.

- Press UP/DOWN to move focus. 
3. Press INFO button to confirm.
4. Repeat the above steps to move more channels.

Sort Channel

- Press BLUE button enter edit mode. Press RED button, the will display sort list.

- Press UP/DOWN select a sort style. Press OK button to confirm.

- Press EXIT button exit edit mode.

Rename Channel

Press BLUE button enter edit mode. Press GREEN button. Select the program to rename the channel with the keyboard.

Delete a Channel

1. Press BLUE button enter edit mode, press BLUE button the Select the program you want delete, press BLUE button then press EXIT button to exit edit mode, the program will be deleted.
2. Repeat the previous step to select more programs to delete.

Favorite Channel

- Press FAV button, then seleet the program you would like set favorite, the will display favorite list.

- Prsee UP/DOWN to select you would like set style.

- Press OK button to confirm.

- Press EXIT button exit favorite list.

- Press FAV button exit FAV mode

4.1.2 EPG (Electronic Program Guide)

The EPG is an on-screen TV guide that shows scheduled programs seven days in advance for every tuned channel. Press the EPG button on the Remote Control to access guide. You can use the UP/DOWN key to select the preferred program. If there is more than one day of the information, Press RIGHT to select one day of the information, then press RIGHT to select one information, the you can press OK button show the information detail or press GREEN to schedule a view or record.

## 4.2 Search

To access the menu, press MENU and select [Search]. The Menu provides options to adjust the search settings. Select an option and press RIGHT/LEFT to adjust the settings. Press EXIT to exit the Menu.

4.2.1 Auto Search

Auto search all frequency

4.2.2 Manual Search

You can select one frequency to search channel

4.2.3 Country

You can select country to change frequency list.

4.2.4 Antenna Power

If you select on, the antenna power will open.

4.2.4 FAT Only

If you select Yes, the will only search FTA program.

## 4.3 System

To access the Menu, press MENU then select [System]. The Menu provides options to adjust the system settings. Press UP/DOWN to select an option and press RIGHT/LEFT to adjust that setting. Press EXIT to exit the menu.

4.3.1 Language

Set OSD Language,First Audio Language,Second Audio Language,Subtitle Language, Teletext.

4.3.2 AV Setting

- Set the TV System to PAL,NTSC.

- Set Video Resolution to [1080i],[1080p],[720p],[576p] for PAL,[576i] for PAL,[480p] for NTSC, [480i] for NTSC.

- Set Apsect Mode to [Atuo],[16:9],[4:3PanScan],[4:3LetterBox].

- Viewo Effects you can choose to Standard, Default, Vivid.

- Audio Out yon can choose to LPCM Out(for dobly), BS Out.

- Scart Out you can choose to CVBS, RGB.

- Play Mode you can choose to Stable, AV Sync.

4.3.3 Lock Time Setting

You can setting date, time, time zone, and summer time.

4.3.4 Timer Setting

- You can schedule the channel to View or Record.

4.3.5 Parental Lock

- You can change Age Limit to View All, 7-year, 12-year, 15 year, 18 year, Lock All.

- You can set Menu Lock

- You can set Channel Lock

- You can set the STB new passwork.

4.3.6 OSD Setting

- You can set Subtitle Display.

- You can set OSD Timeout.

- You can set OSD Transparency.

4.3.7 Favorite

You can rename favorite name.

## 4.4 Tools

To access the Menu, press MENU and select [Tools]. The Menu provides options to adjust the tool settings. Press UP/DOWN to select an option and press RIGHT/LEFT to adjust that setting. Press EXIT to exit the menu.

4.4.1 Information

View model, hardware and software information.

4.4.2 Factory Setting

Reset your Set Top Box to the Default Factory Settings. In Main Menu select [Factory Setting] and press OK or RIGHT to select. Enter your password or the default password '0000' and press OK to confirm. This option will delete all preset channels and settings.

4.4.3 USB Update

Select to start software update if USB is connecting and there's a upgrading file.

4.4.4 USB Backup

Select to start backup software or user DB if USB is connecting and there's a upgrading file.

## 4.5 Media Center

To access the Menu, press Media button on the remote control. The menu provides options to Movie and playback Music and Photo files、Record Files; it can support MP3, JPEG, BMP files. It will only support USB device with FAT and FAT32 file system. It will not support NTFS file system.

4.5.1 Music/Picture/Movie/Record

you can select the Music or Photo type in this menu and press OK to enter the file browser and select the file to playback

4.5.2 Storage Format

You can format the selected disk.

4.5.3 DVR Configuration

You can slect PVR Partition.

## 4.6 Network

To access the Menu, press MENU and select [Network]. The Menu provides options to adjust the tool settings. Press UP/DOWN to select an option and press RIGHT/LEFT to adjust that setting. Press EXIT to exit the menu.

4.6.1 Wifi

Insert Wifi Device, then appear “Wifi device plug in” , Press OK and select Search, Select your Wifi and enter password, connect Wifi.If Wifi Device not insert, the warning message “Wifi device not exist!”.

4.6.2 Online Movie App

If Wifi is connected,Press OK will show youtube app,else the warning message "Wifi:(not connected)" will appear.

Importer: PAZ Media Kft (Veres P. út 511163 Budapest Hungary)

Manufacturer: Shenzhen Joyan Digital Technology Co., Ltd

| Problem | Potential Reasons | What to do |
| --- | --- | --- |
| No picture | Power isn't connected | Connect the power |
|  | The power switch is not on | Switch on the power |
| Screen shows No Signal | Not connect DVB-T cable | Plug in the DVB-T cable |
|  | Incorrect setting | Set up correct parameter |
| No sound from Speaker | No or incorrect connection with audio cable | Connect the audio cable correctly |
|  | Mute the sound | Switch on the correct volume control |
|  | Incorrect sound track | Try another sound track |
| Only sound, no image on the screen | No or incorrect connection with AV cable | Connect the audio cable correctly |
|  | The program is a radio program | Press <TV/RADIO> key to shift into TV mode |
| Remote control unit is not workable | The battery is exhausted | Change new battery |
|  | Remote control unit is not in the right opposite of the front panel or too far from it | Adjust the way of holding remote control unit and near from the panel |
| The image stop suddenly or mosaic | The signal is too weak | Strengthen the signal |

5. Troubleshooting

# 6. Technical Specifications

| Item | Specification |
| --- | --- |
| Tuner | Frequency Range | VHF Band:174 MHz ~230MHz UHF Band:470 MHz ~868MHz |
|  | Bandwidth | 6MHz, 7MHz, 8MHz, |
|  | Input Impedance | 75Ohm |
|  | Signal Input Level | -65 ~ -25dBm |
|  | RF Power Output | 5V,Max 100mA |
| Demodulation | Demodulator | QPSK/16QAM/64QAM/256QAM |
|  | Guard Intervals | 1/4,19/256,1/8,19/128,1/16,1/32,1/128 |
|  | Code Rate | DVB-T:Viterbi+ReedSolomon 1/2,2/3,3/4,5/6,7/8 DVB-T2:LPDC+BCH 1/2,3/5,2/3,3/4,4/5,5/6 |
| Connections | ATN IN | IEC169-2 Female |
|  | LOOP OUT | IEC169-2 Male |
|  | USB | USB 2.0(5V,Max 500mA) |
| Power | Input | DC IN 5V1.5A |
|  | Consumption | Max 7.5W |
| Display | Decoder Module | PAL,NTSC |
|  | Resolution | 720X576(PAL),720X480(NTSC),720P,1080i 480i,480P,576i,576P,1080P |
| Decoding | Aspect Rate | 4:3(Letterbox, Pan& Scan)16:9 |
|  | Video | MPEG2 Transport MP@ML.HL |
|  |  | MPEG4 AVC/H.264 HP@L4 |
|  | Audio | MPEG2 Audio Layer I&II |
| Others | Compliance | Standard DVB-T (EN 300 744) & DVB-T2 (EN 302 755) |
|  | Sound Mode | Right, Left, Stereo |